## Slide 1: Spectrum Valuation
Implications for Sharing and Secondary Markets
Marcela M. Gómez University of Pittsburgh | Martin B.H. Weiss University of Pittsburgh | William Lehr MIT | Giulia McHenry

## Slide 2: How much is electromagnetic spectrum worth?
Image source: https://www.earnware.com/wp-content/uploads/2017/12/What-Are-Email-Subscribers-Worth-Per-Month-2.jpg
Notes: This is the question that framed our discussions.

## Slide 3: $/MHz-POP has become an increasingly noisy indicator for spectrum value
  Traditional drivers of spectrum value have become less relevant
  New technologies and architectures
    Spectrum sharing
    Dynamic Spectrum Access
    Small-cell architecture
    Commercialization of millimeter wave spectrum
Notes: So far, we have relied on a common measure $/MHz-pop, however it seems to have become an increasingly noisy indicator for spectrum value.
This stems from the fact that traditional drivers of value have become less relevant, specially if we consider new technologies and architectures such as spectrum sharing, DSA, small cells and more recently, the commercialization of mmWave spectrum.

## Slide 4: Objective
Discuss the aspects that should enter the spectrum value equation.
Considering:
  Spectrum sharing trends
  A future with viable secondary spectrum markets
  Technical, Economic and Regulatory implications
Notes: Within this context, the objective of our work has been

## Slide 5: Background on Spectrum Value

## Slide 6: Spectrum is an input in the means of production.
Its value is derived from the value of the products and services generated by using the spectrum

## Slide 7: About Spectrum…
National resource managed by the government
(Infinitely) renewable resource
  Spectrum quantity is constant
  Capacity has increased with state of technology, markets and regulatory policies

## Slide 8: Spectrum Management Challenge
Maximize total usage-value realized from spectrum resources over time
Options
  Efficient markets
    Ensure spectrum is directed to highest-value uses over time
    Adjust to changes in market and technical conditions
  Commoditize spectrum
    Potentially through confluence of evolving technical, market and policy forces
    Very difficult due to characteristics of spectrum

## Slide 9: Why is spectrum difficult to commoditize?
Factors that differentiate spectrum resources

## Slide 10: Physics

## Slide 11
Propagation characteristics
Certain regions of electrospace are more desirable for economically valuable applications
  Coverage/capacity tradeoffs
  Options for antenna design
  Network architecture choices, etc.
Why is spectrum difficult to commoditize?

## Slide 12: Technology State of the Art

## Slide 13
Support valuable uses across a wider range of spectrum bands
  Frequency bands become closer (if still imperfect) substitutes.
    Networking context
  Reduce scarcity
Reduce the advantage of operating in particular bands
  Work-arounds to physical differences
  Unbundle applications from frequencies
  Software and Hardware enabling frequency agile radios
Why is spectrum difficult to commoditize?

## Slide 14: Policy and Regulatory Legacy

## Slide 15
License agreements constrain services and business models.
  Limit spectrum substitutability
  Limit potential to reallocate spectrum to higher-value uses
Command-and-Control vs. Market-oriented and resource sharing methods
  Re-think allocation of spectrum rights bundles
    Continuum between exclusive-use and commons extremes
  Consider incumbents governed by legacy rules
‘Patchwork’ of Legal Rights
  Intricate rights systems
Why is spectrum difficult to commoditize?

## Slide 16: How is license value estimated?
Notes: For us to be able to discuss how spectrum should be valued now, it is important to look into ways currently used to value spectrum.

## Slide 17: Potential Value Estimation Methods
Analysis of transaction data to determine market value of spectrum bundles
1
General equilibrium model of supply and demand
2
Estimate market equilibrium price for spectrum
Cost model to estimate net profits from a band
3
Infer spectrum value from changes in value of other assets
4
Hybrid approach
5

## Slide 18: $/MHz- POP

## Slide 19: $/MHZ-POP
Characteristics:
  Normalized metric
    Converts transaction values for bundles of rights into normalized spectrum price metric.
  Computation
    Divide the total value of a spectrum transaction ($) by normalized quantity metric – number of MHz in license times population in license coverage area

## Slide 20: $/MHz-POP
Characteristics:
  Captures key features to determine private value of spectrum rights transferred via spectrum transactions.
    Large frequency range -> more spectrum -> higher capacity
    Large geographical area -> more coverage -> higher revenue
  Leveraged to compare values across individual license and estimate value of unique licenses.
  Used as the basis for econometric modeling

## Slide 21: $/MHZ-POP
Benefits
  Comparability across
    Spectrum transactions
    Frequency bands
    Geographic areas
    Time…
  Allows to*:
    Estimate the normalized value of any wireless broadband spectrum license
    Compare it to other bands
    Convert it to the total license value
  * provided we make specific adjustments for the unique characteristics of a spectrum license

## Slide 22: Challenges
Spectrum license profitability not directly observable
Lack of transactional data
Complexity of modeling costs or revenues from services.
Development of more complex networks (e.g., 5G)

## Slide 23: Market and Technical Trends
Shaping current Telecom Environment

## Slide 24: Spectrum Sharing— The only feasible future
Consider nuances between the exclusive-use vs. shared spectrum poles
  Different definitions of property rights
  Create specialized bundles of rights
    Adapt to services and requirements of incumbents and new entrants
    “Patchwork of rights”
Complex sharing and rights arrangements
  Diversified rights regimes
    More factors affect the definition of rights
  Diverse entities with reduced priorities or obligations to share

## Slide 25: Spectrum Sharing— The only feasible future
Cost/benefit analysis becomes more complex
  How do we properly define the value of specific resources?
New challenge includes navigating through rights’ patchwork and assembling resources that can satisfy different types of services.
As operators increase use of unlicensed or shared spectrum, $/MHz-POP offers a less reliable basis for economic and social value of spectrum.
  Operators need to account for added value
    Complementary resources across diverse bands and regulatory regimes.

## Slide 26: Current Technologies
Sharing and technologies go hand in hand
  Technologies should
    Help identify sharing opportunities
    Detect violations in more constrained and variable settings
    Reduce transaction and sharing costs

## Slide 27: Current Technologies
Millimeter-Wave Spectrum
Expand capacity of existing broadband networks
Particular physical characteristics
New factors in valuation equation
Investments related to coverage capabilities
Opportunities for spectrum re-use
Small-cell networks
Facilitate spatial reuse of spectrum
Line of sight and distance-propagation become less important
Consider sensitivity to placement/orientation of base stations
Trade-off: cost savings from user-deployed small cells vs. losses in spectral efficiency
Dynamic Spectrum Management Capabilities
Allow spectrum users to enter and leave local markets dynamically
Requirements:
Better capabilities to track and enforce rights assignments
Frequently updated maps of transmission opportunities
Identify and asses value of alternative rights bundles
Notes: Spectral efficiency is very sensitive to the placement/orientation of base stations
Increase opportunities for spectrum use – whether it is by identifying areas where spectrum goes unused, maximizing the opporutnities for spectrum reuse, or expanding the capacity of existing networks.

## Slide 28: What does the future look like?
Notes: Given all these market and technical tendencies, what does the future of spectrum valuation look like.

## Slide 29: Spectrum is an input in the means of production.
Its value is derived from the value of the products and services generated by using the spectrum
Notes: A brief reminder:

## Slide 30: Future Spectrum Use
Spectrum-as-a-Service
Spectrum detached from specific and unique services
Opportunities for the deployment of more robust secondary markets

## Slide 31: Successful shared future
Efficiently match supply and demand
Help small and big participants to offer/obtain resources
Approaches:
  Leverage information from database systems
  Increase resource availability via technologies like virtualization
  Efficient middleman/brokerage system
  Secondary Markets

## Slide 32: New Valuation Metric Attributes
Demand factors
  User requirements for wireless information transfer
    Users = point sources that send and/or receive packets of digital information
      Traffic demand dependent on underlying social and economic activity
        Complex wireless networks imply that not all transmissions are equally valuable
Supply factors
  Dependent on system architecture, frequency band, governance mechanisms…
  Capacity provided in variety of ways
    Managed via database systems
    Increased via virtualization…
Notes: Attributes of a less noisy and more useful valuation metric
Users -> point sources that send and/or receive packets of digital information

## Slide 33: Toward alternative valuation measures
Goal:
  Valuation metrics that adjust to the differences in supply and demand stemming from heterogeneous spectrum use
What should we consider?
  Measure that captures density of usage more directly (instead of POP)
  Spatial variation metrics
    Possible re-definition of pixelation
  Variation of private value of licensed spectrum

## Slide 34: Secondary Markets

## Slide 35: Secondary Markets
Increasingly important to dynamically access heterogeneous spectrum resources
Technology and market ecosystem emerging to render heterogeneous spectrum increasingly complementary and substitutable
  Higher social cost of failing to dynamically reallocate spectrum
  Alterations in value may render auction assignments suboptimal
    Secondary markets become key
Still not popular due to lack of potential buyers and sellers
  Lack of consensus on how spectrum should be valued

## Slide 36: Secondary Markets
With better secondary markets
  Facilitate the transition to more efficient spectrum management regimes
  Allow for greater sharing among heterogeneous network operators
  Use market forces to repartition or assemble rights bundles that more closely match market conditions
  Obtain useful spectrum pricing data
    Feedback for markets to continue evolving and improving liquidity

## Slide 37: Conclusions

## Slide 38
$/MHz-POP has become a noisy metric for assessing value
New technologies and market structures
  More opportunities for shaping the shared spectrum future
  Challenges in assembling rights bundles
  Challenges in assessing the value of rights bundles
Time to restart the conversation on secondary markets?
  Flexible-use spectrum put to highest value use
  Offer improved signals to policymakers on spectrum value

## Slide 39: Spectrum Valuation
Implications for Sharing and Secondary Markets
Marcela M. Gómez University of Pittsburgh | Martin B.H. Weiss University of Pittsburgh | William Lehr MIT | Giulia McHenry